## Slide 1: DXS Optics Simulation
Nan Wang, Mar 25th 2021

## Slide 2: Outline
HHLM
  Minimum sampling resolution requirement
  Simulation results
HHLM+HRM
  Sampling resolution
  Simulation results
Reduce vertical dimension for crystal only
  Reduced sampling resolution
  HHLM results
Reduce for all
To-do

## Slide 3: HHLM sampling resolution requirement
Input Parameters |  |  | Si 220 |  |  |  |  |  |  | 
E (eV) | 9481 |  | Bragg angle |  | 19.90988 |  | x_scaling | 12.00 |  | 
T (fs) | 20 |  | asymmetry angle |  | 17 |  | t_stretching (fs) | 52300.88 |  | 
X range (m) | 4.00E-03 |  | b factor 1 |  | 11.83014 |  | z_scaling | 65.00 |  | 
Y range (m) | 4.00E-03 |  | stretch factor 1 |  | 3.922566 |  |  |  |  | 
T range (fs) | 800 |  |  |  |  |  |  |  |  | 
T res (fs) | 2 |  | Unit Time (s) |  | 6.00E-07 |  | Max pts | 2.05E+09 |  | 
E range (eV) | 2 |  | Total time |  | 0:23:28 |  |  |  |  | 
E res (eV) | 0.005 |  | HRM only |  | 0:02:10 |  |  |  |  | 
Nx | 256 |  |  |  |  |  |  |  |  | 
Ny | 8 |  | Ny reduced | 8 |  |  |  |  |  | 
Nz | 400 |  |  |  |  |  |  |  |  | 
 | incident (CRL0) |  | HHLM1 |  | HHLM2 |  | HHLM3 |  | HHLM4 | 
X range, res (um) | 4000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 4000.00 | 3.91
Y range, res (um) | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00
T range, res (fs) | 800.00 | 2.00 | 52000.00 | 2.00 | 52000.00 | 2.00 | 52000.00 | 2.00 | 52000.00 | 2.00
E range, res (meV) | 2000.00 | 5.00 | 2000.00 | 0.08 | 2000.00 | 0.08 | 2000.00 | 0.08 | 2000.00 | 0.08
Nx | 256 |  | 3072 |  | 3072 |  | 3072 |  | 1024 | 
Ny | 8 |  | 8 |  | 8 |  | 8 |  | 8 | 
Nz | 400 |  | 26000 |  | 26000 |  | 26000 |  | 26000 | 
pts | 8.19E+05 |  | 6.39E+08 |  | 6.39E+08 |  | 6.39E+08 |  | 2.13E+08 | 
Estimated time | 0:00:00 |  | 0:06:24 |  | 0:12:47 |  | 0:19:11 |  | 0:21:18 | 
If the vertical direction is suppressed, we can calculate down to about 3fs. My 3fs simulation has pended at NERSC for a few days now due to low priority.
I think the vertical direction can be further reduced to 4 pts, but Oleg mentioned that too few points may not be physical, and that he will be developing a 2D module.

## Slide 4: HHLM results, 1
input
After CRL0
After HHLM1

## Slide 5: HHLM results, 2
After HHLM2
After HHLM3
After HHLM4

## Slide 6: Horizontal sampling issue
1/3
normal

## Slide 7: HHLM+HRM sampling resolution
Input Parameters |  |  | Si 220 |  |  |  |  |  |  |  | Si 440 |  |  |  |  |  |  |  |  |  |  |  |  | 
E (eV) | 9481 |  | Bragg angle |  | 19.90988 |  | x_scaling | 12.00 |  |  | Bragg angle |  | 42.92648 |  | x_scaling | 4.00 |  |  |  |  |  |  |  | 
T (fs) | 800 |  | asymmetry angle |  | 17 |  | t_stretching (fs) | 52300.88 |  |  | asymmetry angle |  | -29.5 |  | t_stretching (fs) | 9381.00 |  |  |  |  |  |  |  | 
X range (m) | 4.00E-03 |  | b factor 1 |  | 11.83014 |  | z_scaling | 2.00 |  |  | b factor 1 |  | 0.243565 |  | z_scaling | 1.00 |  |  |  |  |  |  |  | 
Y range (m) | 4.00E-03 |  | stretch factor 1 |  | 3.922566 |  |  |  |  |  | stretch factor 1 |  | 0.703575 |  |  |  |  |  |  |  |  |  |  | 
T range (fs) | 32000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T res (fs) | 80 |  | Unit Time (s) |  | 6.00E-07 |  | Max pts | 2.05E+09 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E range (eV) | 0.05 |  | Total time |  | 0:27:00 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E res (eV) | 0.000125 |  | HRM only |  | 0:05:46 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nx | 256 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ny | 256 |  | Ny reduced | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nz | 400 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | incident (CRL0) |  | HHLM1 |  | HHLM2 |  | HHLM3 |  | HHLM4 |  | HRM1 |  | HRM2 |  | CRL1 |  | Slit |  | CRL2 |  | HRM3 |  | HRM4 | 
X range, res (um) | 4000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 4000.00 | 3.91 | 4000.00 | 3.91 | 16000.00 | 15.63 | 16000.00 | 15.63 | 16000.00 | 15.63 | 16000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63
Y range, res (um) | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63
T range, res (fs) | 32000.00 | 80.00 | 64000.00 | 80.00 | 64000.00 | 80.00 | 64000.00 | 80.00 | 64000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00
E range, res (meV) | 50.00 | 0.13 | 50.00 | 0.06 | 50.00 | 0.06 | 50.00 | 0.06 | 50.00 | 0.06 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13
Nx | 256 |  | 3072 |  | 3072 |  | 3072 |  | 1024 |  | 1024 |  | 1024 |  | 1024 |  | 1024 |  | 1024 |  | 256 |  | 256 | 
Ny | 256 |  | 256 |  | 256 |  | 256 |  | 256 |  | 256 |  | 256 |  | 256 |  | 256 |  | 256 |  | 256 |  | 256 | 
Nz | 400 |  | 800 |  | 800 |  | 800 |  | 800 |  | 400 |  | 400 |  | 400 |  | 400 |  | 400 |  | 400 |  | 400 | 
pts | 2.62E+07 |  | 6.29E+08 |  | 6.29E+08 |  | 6.29E+08 |  | 2.10E+08 |  | 1.05E+08 |  | 1.05E+08 |  | 1.05E+08 |  | 1.05E+08 |  | 1.05E+08 |  | 2.62E+07 |  | 2.62E+07 | 
Estimated time | 0:00:16 |  | 0:06:33 |  | 0:12:51 |  | 0:19:08 |  | 0:21:14 |  | 0:22:17 |  | 0:23:20 |  | 0:24:23 |  | 0:25:26 |  | 0:26:29 |  | 0:26:44 |  | 0:27:00 | 
Due to the increase in vertical dimension, we can only go down to about 100fs if we simulate the entire beamline.
Most of the computing power is wasted in the HHLM.

## Slide 8: HHLM+HRM results, 1
After CRL0
After HHLM1
After HHLM2

## Slide 9: HHLM+HRM results, 2
After HHLM3
After HHLM4
After HRM2

## Slide 10: HHLM+HRM results, 3
Focus
Before HRM3
After HRM4

## Slide 11: Only crystals are reduced
Input Parameters |  |  | Si 220 |  |  |  |  |  |  |  | Si 440 |  |  |  |  |  |  |  |  |  |  |  |  | 
E (eV) | 9481 |  | Bragg angle |  | 19.90988 |  | x_scaling | 12.00 |  |  | Bragg angle |  | 42.92648 |  | x_scaling | 4.00 |  |  |  |  |  |  |  | 
T (fs) | 800 |  | asymmetry angle |  | 17 |  | t_stretching (fs) | 52300.88 |  |  | asymmetry angle |  | -29.5 |  | t_stretching (fs) | 9381.00 |  |  |  |  |  |  |  | 
X range (m) | 4.00E-03 |  | b factor 1 |  | 11.83014 |  | z_scaling | 2.00 |  |  | b factor 1 |  | 0.243565 |  | z_scaling | 1.00 |  |  |  |  |  |  |  | 
Y range (m) | 4.00E-03 |  | stretch factor 1 |  | 3.922566 |  |  |  |  |  | stretch factor 1 |  | 0.703575 |  |  |  |  |  |  |  |  |  |  | 
T range (fs) | 32000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T res (fs) | 80 |  | Unit Time (s) |  | 6.00E-07 |  | Max pts | 2.05E+09 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E range (eV) | 0.05 |  | Total time |  | 0:04:09 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E res (eV) | 0.000125 |  | HRM only |  | 0:03:14 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nx | 256 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ny | 256 |  | Ny reduced | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nz | 400 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | incident (CRL0) |  | HHLM1 |  | HHLM2 |  | HHLM3 |  | HHLM4 |  | HRM1 |  | HRM2 |  | CRL1 |  | Slit |  | CRL2 |  | HRM3 |  | HRM4 | 
X range, res (um) | 4000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 4000.00 | 3.91 | 4000.00 | 3.91 | 16000.00 | 15.63 | 16000.00 | 15.63 | 16000.00 | 15.63 | 16000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63
Y range, res (um) | 4000.00 | 15.63 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 15.63 | 4000.00 | 500.00 | 4000.00 | 500.00
T range, res (fs) | 32000.00 | 80.00 | 64000.00 | 80.00 | 64000.00 | 80.00 | 64000.00 | 80.00 | 64000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00 | 32000.00 | 80.00
E range, res (meV) | 50.00 | 0.13 | 50.00 | 0.06 | 50.00 | 0.06 | 50.00 | 0.06 | 50.00 | 0.06 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13 | 50.00 | 0.13
Nx | 256 |  | 3072 |  | 3072 |  | 3072 |  | 1024 |  | 1024 |  | 1024 |  | 1024 |  | 1024 |  | 1024 |  | 256 |  | 256 | 
Ny | 256 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 256 |  | 256 |  | 256 |  | 8 |  | 8 | 
Nz | 400 |  | 800 |  | 800 |  | 800 |  | 800 |  | 400 |  | 400 |  | 400 |  | 400 |  | 400 |  | 400 |  | 400 | 
pts | 2.62E+07 |  | 1.97E+07 |  | 1.97E+07 |  | 1.97E+07 |  | 6.55E+06 |  | 3.28E+06 |  | 3.28E+06 |  | 1.05E+08 |  | 1.05E+08 |  | 1.05E+08 |  | 8.19E+05 |  | 8.19E+05 | 
Estimated time | 0:00:16 |  | 0:00:28 |  | 0:00:39 |  | 0:00:51 |  | 0:00:55 |  | 0:00:57 |  | 0:00:59 |  | 0:02:02 |  | 0:03:05 |  | 0:04:08 |  | 0:04:08 |  | 0:04:09 | 
If we only reduce the vertical dimension for the crystals, we can technically save a huge amount of computing power. In this situation, the most extensive components are the two CRLs in the HRM.
I have not finished debugging this simulation yet, mostly because I want to be sure that the simulation is correct when we scale the vertical dimension back up. The following slides will show a comparison between reduced/unreduced results for the HHLM.

## Slide 12: HHLM reduced results comparison, HHLM1
full
reduced

## Slide 13: HHLM reduced results comparison, HHLM2
full
reduced

## Slide 14: HHLM reduced results comparison, HHLM3
full
reduced

## Slide 15: HHLM reduced results comparison, HHLM4
full
reduced
Is this good enough?

## Slide 16: All reduced
Input Parameters |  |  | Si 220 |  |  |  |  |  |  |  | Si 440 |  |  |  |  |  |  |  |  |  |  |  |  | 
E (eV) | 9481 |  | Bragg angle |  | 19.90988 |  | x_scaling | 12.00 |  |  | Bragg angle |  | 42.92648 |  | x_scaling | 4.00 |  |  |  |  |  |  |  | 
T (fs) | 50 |  | asymmetry angle |  | 17 |  | t_stretching (fs) | 52300.88 |  |  | asymmetry angle |  | -29.5 |  | t_stretching (fs) | 9381.00 |  |  |  |  |  |  |  | 
X range (m) | 4.00E-03 |  | b factor 1 |  | 11.83014 |  | z_scaling | 26.00 |  |  | b factor 1 |  | 0.243565 |  | z_scaling | 5.00 |  |  |  |  |  |  |  | 
Y range (m) | 4.00E-03 |  | stretch factor 1 |  | 3.922566 |  |  |  |  |  | stretch factor 1 |  | 0.703575 |  |  |  |  |  |  |  |  |  |  | 
T range (fs) | 2000 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T res (fs) | 5 |  | Unit Time (s) |  | 6.00E-07 |  | Max pts | 2.05E+09 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E range (eV) | 0.8 |  | Total time |  | 0:12:56 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E res (eV) | 0.002 |  | HRM only |  | 0:02:42 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nx | 256 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Ny | 8 |  | Ny reduced | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nz | 400 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | incident (CRL0) |  | HHLM1 |  | HHLM2 |  | HHLM3 |  | HHLM4 |  | HRM1 |  | HRM2 |  | CRL1 |  | Slit |  | CRL2 |  | HRM3 |  | HRM4 | 
X range, res (um) | 4000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 48000.00 | 15.63 | 4000.00 | 1.30 | 4000.00 | 1.30 | 16000.00 | 5.21 | 16000.00 | 5.21 | 16000.00 | 5.21 | 16000.00 | 5.21 | 4000.00 | 5.21 | 4000.00 | 5.21
Y range, res (um) | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00 | 4000.00 | 500.00
T range, res (fs) | 2000.00 | 5.00 | 52000.00 | 5.00 | 52000.00 | 5.00 | 52000.00 | 5.00 | 52000.00 | 5.00 | 10000.00 | 5.00 | 10000.00 | 5.00 | 10000.00 | 5.00 | 10000.00 | 5.00 | 10000.00 | 5.00 | 10000.00 | 5.00 | 10000.00 | 5.00
E range, res (meV) | 800.00 | 2.00 | 800.00 | 0.08 | 800.00 | 0.08 | 800.00 | 0.08 | 800.00 | 0.08 | 800.00 | 0.40 | 800.00 | 0.40 | 800.00 | 0.40 | 800.00 | 0.40 | 800.00 | 0.40 | 800.00 | 0.40 | 800.00 | 0.40
Nx | 256 |  | 3072 |  | 3072 |  | 3072 |  | 3072 |  | 3072 |  | 3072 |  | 3072 |  | 3072 |  | 3072 |  | 768 |  | 768 | 
Ny | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 |  | 8 | 
Nz | 400 |  | 10400 |  | 10400 |  | 10400 |  | 10400 |  | 2000 |  | 2000 |  | 2000 |  | 2000 |  | 2000 |  | 2000 |  | 2000 | 
pts | 8.19E+05 |  | 2.56E+08 |  | 2.56E+08 |  | 2.56E+08 |  | 2.56E+08 |  | 4.92E+07 |  | 4.92E+07 |  | 4.92E+07 |  | 4.92E+07 |  | 4.92E+07 |  | 1.23E+07 |  | 1.23E+07 | 
Estimated time | 0:00:00 |  | 0:02:34 |  | 0:05:07 |  | 0:07:41 |  | 0:10:14 |  | 0:10:43 |  | 0:11:13 |  | 0:11:42 |  | 0:12:12 |  | 0:12:41 |  | 0:12:49 |  | 0:12:56 | 
If we only sample the vertical dimension with 8 pts, we are theoretically able to simulate down to 3fs. However, I don’t know if the results remain physical for the CRLs.

## Slide 17: To-do
SASE simulation
  Oleg doesn’t want me to use obsolete code. Chris is developing a new interface which is close to finish. Will wait for their update.
  Recently acquired access to LCLS Globus endpoint thanks to Wilko
Larger bandwidth
  Maybe you can get higher priority at NERSC? My jobs have pended for quite some time now.
Ask about how to export and import as input wfr
Loop soon, already talking to engineers, so need tolerances/specifications