## Slide 1: DXS Optics Simulation: HHLM
Source
CRL0, 290.0m
HHLM1, 295.0m
HHLM4, 295.68m
HHLM2, 295.18m
HHLM3, 295.5m

## Slide 2: DXS Optics Simulation: HRM
C1, 300.0m
C2, 300.02m
C3, 340.02m
C4, 340.04m
CRL1, 310.02m
CRL2, 330.02m
Slit, 320.02m
CRL0, 290.0m

## Slide 3: Challenge
The challenge of simulating HHLM+HRM together is that:
  HHLM1 has a b-factor of 11.83,
  but C2 has a b-factor of 0.24
The way SRW keeps track of the axes:
  space: resolutionnew = resolutionold * bfactor ; rangenew = resolutionnew * # of pts
  time/energy: resolutionnew = resolutionold
This means the x-axis needs to be expanded in resolution for HHLM1 and then in range for C2. Hence 12 times memory wasted in space.
Also, SRW creates aliasing when decreasing sampling resolution manually, so the number of points per dimension can only increase
Pulse duration (fs) | bandwidth (meV) | HHLM (s) | Ram (GB) | HRM (s) | Ram (GB) | Total (s) | Ram (GB)
1200.0 | 1.51 | 0:00:11 | 0.65 | 0:00:16 | 1.73 | 0:03:03 | 20.77
400.0 | 4.52 | 0:00:26 | 1.95 | 0:00:16 | 1.73 | 0:04:32 | 0.42
20.0 | 90.37 | 0:08:42 | 42.2 | 0:02:31 | 20.77 | 6:19:18 | 2700.55
1.0 | 1807.40 | 2:53:56 | 843.92 | 0:50:19 | 346.22 | 126:26:01 | 54010.92
The numbers in this table are calculated under the following initial conditions: 512 x 8 points in space and a minimum of 1 meV energy resolution. For large bandwidth simulations, the energy resolution can be decreased slightly to accommodate for the maximum ram limit (750 GB at NERSC)
Source
CRL0, 290.0m
HHLM3, 295.5m
HHLM1, 295.0m
HHLM4, 295.68m
HHLM2, 295.18m
C1, 300.0m
C2, 300.02m
C3, 340.02m
C4, 340.04m
CRL1, 310.02m
CRL2, 330.02m
Slit, 320.02m

## Slide 4: Detailed sampling parameter calculation